## Slide 1: Combinational Circuit Analysis
Procedure
  Given a combinational circuit
  Obtain Boolean expressions (one for each output)
  Derive the truth table
  Find out what the circuit does.

## Slide 2: Combinational Circuit Analysis - Examples
w
x
y
z
F
Boolean expression (original)
  F(w, x, y, z) = (x’(y’(w+z) + (y’+w)’))’
Obtain SOP expression
  F(w, x, y, z) =
Obtain minimum SOP expression
  F(w, x, y, z) = x + wy + w’y’z’
Truth Table

## Slide 3: Examples
Derive output expressions
Derive a truth table
•
•
•
•
•
•
a
b
F0
F1
F2
F3

## Slide 4: Examples
a | b | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
F0(a, b) = a’b’ F1(a, b) = a’b F2(a, b) = ab’ F3(a, b) = ab
Truth Table
Output Expressions
What does it do?
A 2-line-to-4-line decoder

## Slide 5: Decoders
3-line-to-8-line Decoders
4-line-to-16-line Decoders
. . . . . . . . . . . . . . .
n-line-to-2n-line Decoders

## Slide 6: Examples
•
•
•
•
•
•
S1
S0
w
x
y
z
out

## Slide 7: Examples
out = w, if S1S0 = 00, = x, if S1S0 = 01, = y, if S1S0 = 10, = z, if S1S0 = 11
w
y
out
S1
x
z
S0
Truth Table
Output Expression:
What does it do?
4 X 1 Multiplexer:
4 input lines
2 select lines
out = S’1S’0 w + S’1S0 x+ S1S’0 y + S1S0 z

## Slide 8: Multiplexers (MUXs)
2 X 1 MUXs
4 X 1 MUXs
. . . . . . . . . . . . . . .
2n X 1 MUXs
2n input lines
n select lines