## Slide 1: Combinational MSI Modules
Multiplexer
works like a single-pole multiple-throw switch.
2nx1 multiplexer (n=3) with 2n binary encoded data
inputs selected by n control inputs, 1-2 enable
inputs, and 1-2 (possibly complemented) output.
Symbol and Truth table: (Fig. 3.20, Table 3.12)

## Slide 2: Combinational MSI Modules (continued)
Implementation of Multiplexer
Truth table Expression and Circuit diagram
(Figure 3.20)

## Slide 3: Combinational MSI Modules (continued)
Use of Multiplexer
Connect multiple sources to a single destination.
Parallel-serial conversion.
Combinational shifter.
General-purpose combinational function generator.
Example 3.13: Implement y(s2,s1,s0)= m1+m2+m4+m5
Solution 1: Use 8x1 MUX with ‘1’ to d1,d2,d4,d5, & ‘0’ to others.
MUX
s2 s1 s0
d0
d1
d2
d3
d4
d5
d6
d7
1
y
Solution 1
MUX
s2 s1
d0
d1
d2
d3
1
s0
y
Solution 2
Solution 2: Use only one 4x1 MUX with s0,s0,1,0 to d1-d3 resp.

## Slide 4: Combinational MSI Modules (continued)
Decoder/Demultiplexer
nx2n decoder (n=3) with n binary coded inputs, 1-2
enable inputs, and 2n mutually exclusive outputs
(minterms) corresponding to the input code.
Symbol and Truth table: (Fig.3.24, Table 3.14)

## Slide 5: Combinational MSI Modules (continued)
Truth table Expression and circuit diagram (Fig.3.24)
Implementation of Decoder/Demultiplexer
mi = Enable1 Enable2 (input code = i) for i=0 to n-1

## Slide 6: Combinational MSI Modules (continued)
Address decoder — select a memory
address or a register number.
Operational decoder — decode instruction
Opcode or microinstruction fields.
Demultiplexer — dispatch a single-source
to one of multiple destinations
Use of Decoder/Demultiplexer

## Slide 7: Combinational MSI Modules (continued)
2nxn encoder (n=3) with 2n inputs and n
binary coded outputs plus a presence bit.
“translate” an active Ii input into its corres- ponding binary code i for i = 0,1,…,n-1.
v=1 validates the output for any input Ii =1.
(Fig.3.26, Table 3.15)
Encoder

## Slide 8: Combinational MSI Modules (continued)
Use of Encoder:
◊ Encode the exception request signals.
◊ However interrupt requests may not be
mutually exclusive, so priority encoder.
Truth table Expression and Circuit diagram
(Fig.3.26. exp.3.39)
Implementation of Encoder
y2=I4+I5+I6+I7
y1=I2+I3+I6+I7
y0=I1+I3+I5+I7
v=I0+I1+I2+I3+I4+I5+I6+I7

## Slide 9: Combinational MSI Modules (continued)
Ii has a higher priority than ij if i>j.
(Table 3.16)
Priority Encoder
(exp.3.40)