## Slide 1: Sequential System
Combinational system
  The output at any instant of time depends only on what the inputs are at that time.
    Small delay is ignored.
Sequential system (finite state machine)
  The output depends not only on the present inputs but also on the past history (memory).
    What has happened earlier.

## Slide 2
General Model of Sequential Circuit
Flip-Flop as Basic Memory Unit
Analysis of Sequential Circuits
Design of Sequential Circuits
Sequential MSI Modules
Sequential Circuit

## Slide 3: Clocked System
Clocked System (synchronous system)
  A clock is a signal that alternates (over time) between 0 and 1 at a regular rate.
  T (on the diagram) is the length of one cycle.
  Frequency is the inverse (1/T). (1 Hz is 1 cycle per second)
    T = 5 nsec = 5 nanoseconds = 5*10-9 second
    F = 1/T = 1/(5*10-9) = 200*106 Hz = 200 MHz (megahertz)
T

## Slide 4: Synchronous Sequential System
Combinational Logic
Memory
Inputs
Outputs
Next state
Present state
Clock
Combinational logic is a function of the system inputs and the contents of the memory.
Outputs of combinational logic are the system outputs and signals to update the memory.
The state changes only at discrete instants of time, typically synchronous to the clock signal.

## Slide 5: Types of Binary Storage Devices
Latch
  Static device, no clock involved.
  Output changes immediately whenever the input changes.
  Used for temporary (buffer) storage.
Flip flop
  Clocked device.
  Output changes shortly after a clock transition (at the edge of the clock).
  Two outputs Q and Q’ (bit stored and its complement).

## Slide 6: SR Latch
A latch is a binary storage device with feedback -- the output of each gate is connected to the input of the other gate. P = (S+Q)’ Q = (R+P)’
S=1, R=0 -- 1 is stored in Q -- S (set) P = (1+Q)’ = 1’ = 0 Q = (0+0)’ = 0’ = 1
S=0, R=1 -- 0 is stored in Q -- R (reset) Q = (1+P)’ = 1’ = 0 P = (0+0)’ = 0’ = 1
S=R=0 -- normal storage state P = Q’ (Therefore, P is labeled as Q’) Q = P’
S=R=1 -- undefined Unpredictable next state (race condition) when S=R=0
•
•
S
R
P
Q
(Q’)
S | R | Q | Q’ | 
1 | 0 | 1 | 0 | Set
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 1 | Reset
0 | 0 | 0 | 1 | 
1 | 1 | 0 | 0 | Undefined

## Slide 7: Waveform of SR Latch
S
R
Q
Q’
Set
Hold
Reset
Forbidden
Set
Hold
Reset
Forbidden
Race

## Slide 8: Gated SR Latch
•
•
SG
Q’
Q
S
R
RG
Gate
•
Gate | S | R | Q(t+1)
0 | X | X | Unchanged
1 | 0 | 0 | Unchanged
1 | 0 | 1 | 0 (Reset)
1 | 1 | 0 | 1 (Set)
1 | 1 | 1 | Undefined

## Slide 9: D Latch
•
•
SG
Q’
Q
D
RG
Gate
•
•
Undefined state in the SR latch is eliminated.
Gate | D | Q(t+1)
0 | X | Unchanged
1 | 0 | 0 (Reset)
1 | 1 | 1 (Set)

## Slide 10: S’R’ Latch (NAND Gate)
•
•
S’
R’
Q’
Q
S’ | R’ | Q | Q’ | 
0 | 1 | 1 | 0 | Set
1 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | Reset
1 | 1 | 0 | 1 | 
0 | 0 | 1 | 1 | Undefined

## Slide 11: Flip Flop
A flip flop is a clocked binary storage device.
  The state will only change on the transition of the clock.
    Trailing-edge triggered -- change takes place when the clock goes from 1 to 0.
    Leading-edge triggered -- change takes place when the clock goes from 0 to 1.
Four types of flip flop
  D, SR, T, and JK flip flop

## Slide 12: SR Master/Slave Flip Flop
•
•
Q
Q’
•
•
•
S
R
Clock
•
•
Master
Slave
X’
X
When the clock is 1, the first flip flop (master) is enabled. When the clock is 0, the second flip flop (slave) is enabled. It is trailing-edge triggered.

## Slide 13: SR (Set-Reset) Flip Flop
S
Q
Q’
Clock
R
S
Q
Q’
Clock
R
S | R | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | --
1 | 1 | 1 | --
S | R | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | --
0
1
01
10
00 01
00 10
SR
Q(t+1) = S + R’ Q(t)
SR =/= 1
not allowed
not allowed
SR
Q(t)
00
01
0
11
10
1
X
1
X
1
1

## Slide 14: Timing Diagram of SR Flip Flop
Clock
CLR’
S
R
Q

## Slide 15: D Flip Flop
D
Q
Q’
Clock
Trailing-edge triggered
D
Q
Q’
Clock
Leading-edge triggered
The output is just the input delayed until the next active clock transition. The triangle is used to indicate which input is the clock. A circle is shown on the clock input of a trailing-edge triggered flip flop.
D | Q(t) | Q(t+1)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
D | Q(t+1)
0 | 0
1 | 1
0
1
0
1
0
1
D
Q(t+1) = D

## Slide 16: Trailing-Edge Triggered D Flip Flop
Clock
D
Q
Q’
Value Q changes shortly after the trailing edge of the clock. Slashed sections indicate the unknown initial values of Q and Q’. D should reach the correct value before the next active clock transition.

## Slide 17: Leading-Edge Triggered D Flip Flop
Clock
D
Q
Q’
Value Q changes shortly after the leading edge of the clock.

## Slide 18: JK Flip Flop
J
Q
Q’
Clock
K
J
Q
Q’
Clock
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q(t)’
0
1
01 11
10 11
00 01
00 10
JK
Q(t+1)= JQ(t)’ + K’Q(t)
JK
Q(t)
00
01
0
11
10
1
1
1
1
1
JK flip flop is a combination of the SR and T.

## Slide 19: Timing Diagram of JK Flip Flop
Clock
CLR’
J
K
Q

## Slide 20: T (Toggle) Flip Flop
Clock
CLR’
T
Q
T
Q
Q’
Clock
T
Q
Q’
Clock
T | Q(t) | Q(t+1)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
T | Q(t+1)
0 | Q
1 | Q’
0
1
1
1
0
0
T
Q(t+1) = T Q(t)

## Slide 21: Two Flip Flops
D
Q
Q’
Clock
D
Q
Q’
•
x
Clock
D
A
B
The output of flip flop r is a replica of that of q, delayed by one clock period.
A
B

## Slide 22: Basic Idea of Pipelining
Clock
•
stands for combinational logic. A group of flip flops store the outputs of combinational logic of the current stage. Clock synchronizes all flip flops.
D
q
q’
D
q
q’
D
q
q’
D
q
q’
D
q
q’
D
q
q’
D
q
q’
D
q
q’
D
q
q’
•
•
D
q
q’
D
q
q’
D
q
q’
•
1
2

## Slide 23: Flip Flop with Clear & Preset Inputs
D
Q
Q’
Clock
PRE’
CLR’
D
Q
Q’
Clock
PRE
CLR
PRE’ | CLR’ | D | Q(t) | Q(t+1)
0 | 1 | X | X | 1
1 | 0 | X | X | 0
0 | 0 | X | X | --
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
static immediate
not allowed
clocked

## Slide 24: Timing for Flip Flop with Clear & Preset
Clock
CLR’
PRE’
D
Q

## Slide 25: Example of Sequential System
A system with one input x and one output z, such that z=1 iff x has been 1 for at least three consecutive clock times.
Analysis
  Information about the last three inputs must be stored in the memory.
  What is stored is the state of the system.
  Memory may consist of a set of binary storage device.

## Slide 26: Describing Sequential System
Two tools
  State table
  State diagram (state graph)
    A graphical representation of the behavior of the system.
  Both of them shows, for each input combination and each state, what the output is and what the next state is.
We refer to the present state as Q(t) and the next state as Q(t+1).

## Slide 27: Timing Trace
A set of values for the input and the output at consecutive clock time.
  Used to clarify the definition of system behavior.
  Inputs are an arbitrary set of values.
Timing trace of the example.
  x 0 1 1 0 1 1 1 0 0 1 0 1 1 1 1 1 0 0
  z ? 0 0 0 0 0 0 1 0 0 0 0 0 0 1 1 1 0 0 0 0
Moore model
  Output depends only on the state of the system (not the present input).

## Slide 28: Implementation of SR Flip Flop
•
•
Q
Q’
•
•
•
S
R
Clock
•
•

## Slide 29: State Table/Diagram of The Example
B
0
C
0
A
0
D
1
1
0
0
0
0
1
1
1
Present | Next | state | 
state | x = 0 | x = 1 | Output
A | A | B | 0
B | A | C | 0
C | A | D | 0
D | A | D | 1
x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  |  | 
q | A | A | B | C | A | B | C | D | A | A | B | A | B | C | D | D | D | A | A |  | 
z | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 30: Implementation of D Flip Flop
•
•
Q
Q’
•
•
•
D
Clock
•
•
•

## Slide 31: Implementation of JK Flip Flop
•
•
Q
Q’
•
•
•
J
K
Clock
•
•
•
•

## Slide 32: Implementation of T Flip Flop
•
•
Q
Q’
•
•
•
T
Clock
•
•
•
•
Q(t+1) = T Q(t) = TQ(t)’+T’Q(t) = JQ(t)’ + K’Q(t)
•